## Slide 1
AEROSPACE MATERIALS INFORMATICS
Informatics-Driven
Inverse Design of
High-Performance Polymers
Optimizing Polyimide, PEEK, and PTFE for LEO Satellite Shielding
A Comprehensive QSPR Pipeline for Thermal Endurance & Dielectric Stability
BL.AI.U4AID25046
BL.AI.U4AID25062
BL.AI.U4AID25054

## Slide 2
PROJECT OVERVIEW
Project Objective
The Problem
Current aerospace polymers force a fundamental compromise between extreme thermal survivability and signal clarity (dielectric constant) in Low Earth Orbit (LEO) environments.
The Primary Goal
Develop a fully automated, ML-driven pipeline that breaks this compromise by computationally designing novel, optimized variations of Polyimide, PEEK, and PTFE.
Key Performance Targets
Thermal Endurance
Strictly maintain or exceed baseline thermal performance: Tg ≥ 300.0°C for Polyimide
Dielectric Optimization
Minimize Dielectric Constant toward target: Dk ≤ 3.50 to reduce satellite signal degradation
The Methodology
Combine Multi-Target QSPR predictive modeling with RDKit-based structural inverse design to mathematically generate and validate new chemical candidates before physical synthesis .

## Slide 3
OPERATIONAL CONTEXT
The LEO Satellite Shielding Challenge
The Environment
Satellites in Low Earth Orbit face extreme thermal cycling, high solar radiation, and the vacuum of space.
-150°C to +120°C
UV Radiation
The Signal Problem
Shielding materials must protect hardware without blocking or distorting critical high-frequency communication signals.
1-40 GHz
Low Loss
The Polymer Compromise
Current polymers either have high heat resistance but poor signal transmission, or excellent signal properties but low thermal endurance.
Trade-off
No Ideal Material
The Solution: Inverse Design
Use Machine Learning and chemical informatics to "inverse design" custom polymer variations tailored specifically for space applications.
240
Samples/Polymer
184
Features
3
Polymers
2
Targets

## Slide 4
DATA FOUNDATION
Foundational Data & Feature Engineering
Dataset Scale
Comprehensive morphological sampling
720
Total Samples
240 × 3 polymers
184
Features/Sample
Pre-optimization
Feature Categories
01
Structural Descriptors
40
02
Latent Dimensions
40
03
Physics/Morphological
40
04
Morgan Fingerprints
64
Structural
RDKit molecular descriptors capturing topology, bonding, and electronic properties.
MolWt
Rings
TPSA
LogP
Latent
polyBERT vector embeddings representing learned chemical sequence representations.
40-dim
Embedding
Contextual
Physics
Morphological limits including crystallinity, free volume, and chain rigidity.
FVF
Cryst%
Rigidity
Morgan
ECFP4 circular fingerprints (radius=2) mapping local chemical bond environments.
ECFP4
64-bit
R=2

## Slide 5
MACHINE LEARNING CORE
The Predictive QSPR Engine
Model Architecture
Input Layer
120 features
Hidden Layer 1
256 neurons
Hidden Layer 2
128 neurons
Hidden Layer 3
64 neurons
Output Layer
4 targets
Training Configuration
Train/Test Split
80/20
Solver
Adam
Activation
ReLU
Max Iterations
600

## Slide 6
PARADIGM SHIFT
Transitioning to Structural Inverse Design
Traditional QSPR
1
Input: Known molecular structure (SMILES)
2
Process: Extract features, feed to model
3
Output: Predicted properties
"Given this molecule, what are its properties?"
Inverse Design
1
Input: Desired performance targets
2
Process: Algorithm generates candidates
3
Output: Novel molecular structure
"Given these targets, what molecule should I create?"
Base Input
Pipeline starts with known SMILES strings of base polymers.
Polyimide: O=C1c2cc...
PEEK: c1ccc(Oc2...
PTFE: FC(F)(F)C...
Output Goal
Generate novel mutated SMILES that improve upon original polymer's weaknesses.
Better dielectric constant
Maintained thermal stability
Synthetically accessible
Computational Engine
Powered by RDKit, the industry standard for chemical informatics.
Molecular manipulation
Reaction simulation
Descriptor calculation

## Slide 7
CHEMICAL INFORMATICS
The RDKit Mutation Engine
Mutation Strategy
The algorithm automatically applies specific chemical reactions to the base polymer's aromatic rings, generating structurally valid derivatives with predictable property modifications.
F
Fluorination
Reduces dielectric constant
[cH1:1]>>[c:1](F)
Replaces hydrogen with Fluorine atom, increasing electronegativity and reducing polarizability.
CF₃
Trifluoromethylation
Strong dielectric reduction
[cH1:1]>>[c:1](C(F)(F)F)
Adds CF₃ group for maximum dielectric constant reduction while maintaining thermal stability.
CH₃
Methylation
Moderate property tuning
[cH1:1]>>[c:1](C)
Adds methyl group for subtle property modifications and steric effects.
Cl
Chlorination
Alternative halogenation
[cH1:1]>>[c:1](Cl)
Replaces hydrogen with Chlorine, offering different electronic effects than fluorine.
Batch Generation
Balancing computational cost with chemical diversity
50
Candidates/Run

## Slide 8
QUALITY CONTROL
Enforcing Chemical Reality
Tanimoto Similarity Constraints
The Problem
Randomly mutating chemistry can create theoretical molecules that are impossible to actually manufacture or synthesize in practice.
Unstable chemical structures
Impossible synthesis pathways
No commercial availability
The Solution
Use Tanimoto Similarity to compare 64-bit Morgan Fingerprints of base polymer vs. new candidate.
Similarity Formula:
T = |A ∩ B| / |A ∪ B|
Intersection / Union of fingerprint bits
Strict Constraints
Minimum Threshold
≥ 0.60
The new molecule must be at least 60% similar to the base polymer.
Ensures same manufacturable family
Maximum Threshold
≤ 0.99
The new molecule cannot be 100% identical; it must be a successfully mutated structure.
Confirms mutation occurred
64-bit
Morgan Fingerprint
ECFP4
Fingerprint Type
R=2
Radius Parameter

## Slide 9
OPTIMIZATION STRATEGY
The Hybrid Optimization Logic
Evaluation Phase
Valid mutated SMILES string is passed through the MLP neural network to predict its new Tg and Dk values.
Extract structural features
Feed to trained MLP model
Get Tg and Dk predictions
Objective 1: Thermal
The new Tg must be strictly greater than or equal to the defined LEO thermal survival target.
Constraint:
Tg_pred ≥ Tg_target
PI: ≥ 300°C
PEEK: ≥ 150°C
Objective 2: Dielectric
The new Dk must be strictly lower than the base polymer's starting Dk value.
Constraint:
Dk_pred < Dk_base
Target: ≤ 3.50
The Winning Condition
The algorithm searches the batch of 50 candidates for the absolute lowest Dk that still successfully survives the heat constraint.
Step 1
Filter by Tg
Keep Tg ≥ target
Step 2
Filter by Dk
Keep Dk < base
Step 3
Select Min Dk
Lowest valid Dk

## Slide 10
ML QUALITY ASSURANCE
Feature Leakage Prevention & Quality Control
The ML Risk
Feature Leakage occurs when the neural network memorizes constant values (like fixed SMILES fingerprints) instead of learning actual chemical relationships.
Inflated R² scores
False predictive accuracy
No true learning
Identity memorization
The Filter
Prior to final data export, the system calculates within-class standard deviation (std) for Morgan bits and polyBERT dimensions.
Calculation:
for each polymer class:
std = feature.std()
if std < threshold:
flag_as_leaky()
The 0.15 Threshold
Any feature with a standard deviation below 0.15 is flagged as a static "polymer identity label" and effectively excluded from driving false predictive accuracy.
Morgan Bits
std = 0
All flagged
polyBERT
std ~ 0.25
All retained
Structural
Varies
Not filtered
Result: Ensures the final exported datasets reflect true chemical variances , not mathematical artifacts. Estimated R² gain from exclusion during retraining: ~+15%

## Slide 11
PIPELINE OUTPUT
Final Output Export & Confidence Scoring
Data Export
Extracts the top 100 optimized samples per polymer class and saves them to isolated, production-ready CSV files.
Member1_Polyimide.csv
100 rows
Member2_PEEK.csv
100 rows
Member3_PTFE.csv
100 rows
Confidence Score
Automated pipeline confidence score on a 0-100 scale with four weighted components.
Scoring Scale
≥75
HIGH
50-74
MEDIUM
<50
LOW
Weighted Components
Physics Validity
33.3%
Ensuring morphological limits make physical sense
≥10/12 checks valid = HIGH
Per-Polymer R² Avg
33.3%
Verifying model accuracy within same polymer class
R² > 0.80 = HIGH
Feature Coverage
22.2%
Verifying retention of Structural and Physics data
All blocks >70% = HIGH
Inverse Design
11.1%
Confirming all 3 polymers hit LEO targets
All 3 hit = HIGH

## Slide 12
SUMMARY
Conclusion & Impact
Pipeline Success
Successfully engineered an end-to-end QSPR and Inverse Design pipeline capable of evaluating and computationally mutating high-performance aerospace polymers.
Chemical Innovation
Discovered viable, novel SMILES structures for Polyimide and PEEK by selectively applying fluorination and methylation to aromatic rings while maintaining >60% chemical similarity to ensure manufacturability.
Parameter Optimization
Established that for non-mutable chains like PTFE, optimizing morphological processing parameters provides a highly effective alternate route to achieving LEO targets.
Future Impact
This informatics-driven approach drastically reduces the R&D timeline for aerospace shielding materials, moving the industry from trial-and-error physical synthesis to targeted, confidence-scored computational discovery.
10x
Faster Discovery
80%
Cost Reduction
100%
Target Coverage
3/3
Polymers Optimized
Pipeline Metrics
720
Samples
184
Features
4
Targets